## Slide 1: Connect the hardware

## Slide 2: Measured vs Expected Results
fin = 2kHz, fsamp = 500kHz Crossover region at 3.8V on OPA316 |  |  |  |  |  |  |  |  |  |  | 
PSI Signal Settings |  | Calculated PSI Min and Max Output |  | OPA316 Expected |  | OPA316 Measured |  | OPA320 Expected |  | OPA320 Measured | 
Vin (Vpp) | Vcm (V) | Vmin (V) | Vmax (V) | SNR (dB) | THD (dB) | SNR (dB) | THD (dB) | SNR (dB) | THD (dB) | SNR (dB) | THD (dB)
2 | 1.5 | 0.5 | 2.5 | 85.3 | -104.4 |  |  | 85.7 | -109.2 |  | 
2 | 2 | 1 | 3 | 85.3 | -102.9 |  |  | 85.6 | -105.9 |  | 
2 | 3 | 2 | 4 | 85.2 | -98.8 |  |  | 85.7 | -106.1 |  | 
2 | 3.2 | 2.2 | 4.2 | 85.2 | -83.8 |  |  | 85.6 | -108.3 |  | 
2 | 3.5 | 2.5 | 4.5 | 85.1 | -76.1 |  |  | 85.6 | -109.1 |  | 
2 | 3.8 | 2.8 | 4.8 | 85.0 | -77.2 |  |  | 85.7 | -106.4 |  | 
Your results should show the same trend as the expected result but the specific values will differ.
Notes: This table shows the expected results for the OPA316 and OPA320. Let’s look at the first row. The input is set to 2Vpp, or 1Vpk. The common mode or offset is set to 1.5V. The sine wave negative peak is at Vcm – Vpk, in this case it’s 1.5V – 1V which is equal to 0.5V. Similarly, the positive peak is 1.5V +1V which is 2.5V. The positive peak, denoted Vmax, is the number we need to pay attention to. When Vmax is below the crossover voltage we will not see crossover distortion and the AC performance should be good. When Vmax is above the crossover voltage we should see crossover distortion and the AC performance should be degraded. The OPA316 crossover region happens at 3.8V, so we should see degradation above this voltage. Sure enough, you can see that the OPA316 THD degrades significantly for Vmax of 4V and greater. Notice, however, that the OPA320 has good performance across all common mode voltages because it is a zero-crossover device.
Now you can run the same experiment for the OPA320 and the OPA316. Your results should have the same trend as the expected results, but the specific value may differ somewhat. For example, you may see a THD of 100dB for Vmax of 2.5V, and 67dB for Vmax of 4.8V. The point isn't to focus on the exact value, but to notice that THD dramatically degrades once you enter the crossover region. If you don’t get these results, make sure that you have adjusted the hardware and software correctly. A common error is to forget to adjust the sampling rate to 500ksps. This is needed as the OPA316 is not fast enough for the ADS8860 full sampling rate of 1Msps.